## Slide 1: Conditional Structures
Computer Organization and Assembly Language
Computer Science Department
National University of Computer and Emerging Sciences Islamabad

## Slide 2: Agenda for today
Arithmetic Instructions
Labels
Conditional and Unconditional Flow of Program
JMP instruction
Loops

## Slide 3: Arithmetic Instructions
MUL operand1
  operand1 is 8-bit (type BYTE): multiply with contents placed in register AL, result will be in AX.
  operand1 is 16-bit (type WORD): multiply with contents placed in register AX, result will be in DX:AX.
  operand1 is 32-bit (type DWORD): multiply with contents placed in register DX:AX, result will be in EDX:EAX.
  Example
  MOV AL, 200 ;
  MOV BL, 4
  MUL BL ;

## Slide 4: MUL Instruction

## Slide 5: Arithmetic Instructions
DIV operand1
  when operand is a BYTE: AL = AX / operand then
    AL =Quotient
    AH = remainder
  Example
  MOV AX, 203;
  MOV BL, 4;
  DIV BL ; AL = 50 , AH = 3

## Slide 6: DIV Instruction
  when operand is a word: AX = (DX AX) / operand then
    AX = Quotient
    DX = remainder

## Slide 7: Divide overflow
If a division operand produces quotient that is larger than storage then divide overflow condition occurs and the program terminates.
  MOV AX,1000h
  MOV BL, 10h
  DIV BL ;AL cannot hold 100h
Similarly when you divide by zero program terminates.

## Slide 8: Labels in Assembly
A label is an identifier that is followed by a colon.
Names suffixed with colons (:) are symbolic labels.
The labels do not create code.
They are simply a way to tell the assembler that those locations have symbolic names.
Example
  Label1:
  Above:
  Start:

## Slide 9: JMP Instruction
Unconditional jump
Jumps to the given label[Address]
Syntax:
  JMP [Label] ;PC will jump to the address of Label

## Slide 10: Examples
Backward jump
  StartLoop:
  ; statements
  JMP StartLoop
Forward jump
  JMP EndLoop
  ; statements
  EndLoop:

## Slide 11: Conditional Jumps
Transfers Control if condition is satisfied.
Jumps based on unsigned data
Jumps to label if equal
  JE [label]
Jump if not equal
  JNE [label]

## Slide 12: Jumps Based on Equality
Notes: ZF=1 ZF=0

## Slide 13: CMP Instruction
Compares value of two operands and set flags
Syntax
  CMP opr1,opr2
  Opr1 = reg/mem
  Opr2 = reg/mem/imme
Example
  CMP ax,bx
  CMP ah,al

## Slide 14
Notes: ZF=1 ZF=0

## Slide 15
Example:
    …
    Mov al,5
    Cmp al,5
    Je label1
    Jmp exit
  Label1:
    Mov ax,bx
    …
  Exit: …

## Slide 16: Jumps Based on Flags

## Slide 17: Jumps Based on Conditions

## Slide 18: Some Conditional Jumps
Ja – jump if dest above src
Jb – jump if dest below src
Unsigned integers
ZF = 0 and CF = 0
CF = 1

## Slide 19: Some Conditional Jumps
Jl – jump if Sdest lower than Ssrc
Jg – jump if dest greater than src
Signed integers
ZF ≠ CF
ZF = 0 and SF = OF

## Slide 20: Your turn . . .
Implement the following pseudocode in assembly language. All values are unsigned:
if( bx <= ax
&& cx > dx )
{
ax = 5;
dx = 6;
}
(There are multiple correct solutions to this problem.)

## Slide 21: Block-Structured IF Statements
Assembly language programmers can easily translate logical statements written in C++/Java into assembly language. For example:
  mov ax,op1
  cmp ax,op2
  jne L1
  mov X,1
  jmp L2
L1:
mov X,2
L2:
if( op1 == op2 )
X = 1;
else
X = 2;

## Slide 22: Your turn . . .
Implement the following pseudo code in assembly language. All values are 16-bit signed integers:
if( var1 == var2 )
var3 = 10;
else
{
var3 = 6;
var4 = 7;
}
(There are multiple correct solutions to this problem.)

## Slide 23: Another Example

## Slide 24: And Another
  mov ax,var1
  cmp ax,var2
  je L1
  mov var3,6
  mov var4,7
  jmp L2
L1: mov var3,10
L2:
if( var1 == var2 )
var3 = 10;
else
{
var3 = 6;
var4 = 7;
}

## Slide 25: Execution of Another example
;;Assembly language code
mov ax , 15
mov bx , 15
mov cx , 0
cmp ax , bx
jne lable1
mov cx , ax
jmp end
lable1:
mov cx , bx
end:
;;Assembly language code
mov ax , 15
mov bx , 10
mov cx , 0
cmp ax , bx
jne lable1
mov cx , ax
jmp end
lable1:
mov cx , bx
end:

## Slide 26: Loop Instruction
CX used as Counter
Automatically Decremented after every iteration
Label is used to jump
Ends when counter reaches zero
Example:
  MOV cx,10 ;loop runs 10 times
  Loop1:
    …
  Loop Loop1

## Slide 27: WHILE Loops
while( ax < bx)
ax = ax + 1;
A WHILE loop is really an IF statement followed by the body of the loop, followed by an unconditional jump to the top of the loop. Consider the following example:
top: cmp ax,bx ; check loop condition
jae next ; false? exit loop
inc ax ; body of loop
jmp top ; repeat the loop
next:
This is a possible implementation:

## Slide 28: Another Example