## Slide 1: COMPUTER ARITHMETIC
Floating Point Representation
Computer Science Department
National University of Computer and Emerging Sciences
Islamabad
Notes: 1

## Slide 2: REAL NUMBERS
Numbers with fractions
Could be done in pure binary
  1001.1010 = 24 + 20 +2-1 + 2-3 =9.625
Where is the binary point?
Fixed?
  Very limited
Moving?
  How do you show where it is?
Notes: 2

## Slide 3: FLOATING POINT NOTATION
Decimal
  12.4568ten (decimal notation) means
      10*1 + 2 + 4/10 + 5/100 + 6/1000 + 8/10000
  In scientific notation
    12.4568 =
      124568 * 10-4 = 1245680 * 10-5 =
      12456.8 * 10-3 = 1245.68 * 10-2 =
      124.568 * 10-1 =12.4568 * 100
      1.24568 * 101
    1.24568*101 is an example of normalised scientific notation.
Notes: 3

## Slide 4: FLOATING POINT IN BINARY
Binary
  0.010011two =
    (0/2) + (1/22) + (0/24) +(1/25) + (1/26)
      0 + 1/4 + 0 + 1/32 + 1/64 =
      (0.25 + 0.03125 + 0.015625)ten =
      0.296875ten
In scientific notation
  10011*2-6 = 1001.1*2-5 =
  100.11*2-4
  1.0011*2-2 normalised
Notes: 4

## Slide 5: NORMALIZATION
Every binary number, except the one corresponding the number zero, can be normalized by choosing the exponent so that the radix point falls to the right of the leftmost 1 bit.
37.2510 = 100101.012 = 1.0010101 x 25
7.62510 = 111.1012 = 1.11101 x 22
0.312510 = 0.01012 = 1.01 x 2-2

## Slide 6: FLOATING-POINT REPRESENTATION
Computers use a form of scientific notation for floating-point representation
Numbers written in scientific notation have three components:
Notes: 6

## Slide 7: FLOATING POINT
+/- .significand x 2exponent
Point is actually fixed between sign bit and body of mantissa
Exponent indicates place value (point position)
Sign bit
Biased
Exponent
Significand or Mantissa
Notes: 7

## Slide 8: FLOATING-POINT STANDARDS
The IEEE has established a standard for
floating-point numbers
The IEEE-754 single precision floating point
standard uses an 8-bit exponent (with a bias of 127) and a 23-bit significand. Bias is 2k-1-1
The IEEE-754 double precision standard uses an 11-bit exponent (with a bias of 1023) and a 52-bit significand.
Notes: 8

## Slide 9: FLOATING-POINT REPRESENTATION
In both the IEEE single-precision and double-
precision floating-point standard, the significand has an implied 1 to the LEFT of the radix point.
  The format for a significand using the IEEE format
  is: 1.xxx…
  For example, 4.5 = .1001 x 23 in IEEE format is 4.5 = 1.001 x 22.
  The 1 is implied, which means it does not need to be
  listed in the significand (the significand would include
  only 001).
Notes: 9

## Slide 10: FLOATING-POINT REPRESENTATION
Example: Express -3.75 as a floating point number
using IEEE single precision.
First, let’s normalize according to IEEE rules:
  -3.75 = -11.112 = -1.111 x 21
  The bias is 127, so we add 127 + 1 = 128 (this is our
  exponent)
  The first 1 in the significand is implied, so we have:
  Since we have an implied 1 in the significand, this equates to
    -(1).1112 x 2 (128 – 127) = -1.1112 x 21 = -11.112 = -3.75.
(implied)
Notes: 10

## Slide 11: DECIMAL FLOATING POINT TO IEEE STANDARD CONVERSION
Ex 1: Find the IEEE FP representation of 40.15625
Step 1.
Compute the binary equivalent of the whole part and the fractional part. (i.e. convert 40 and .15625 to their binary equivalents)

## Slide 12: DECIMAL FLOATING POINT TO IEEE STANDARD CONVERSION
40 .15625
Result: Result:
101000 .00101
So: 40.1562510 = 101000.001012

## Slide 13: DECIMAL FLOATING POINT TO IEEE STANDARD CONVERSION
Step 2. Normalize the number by moving the decimal point to the right of the leftmost one.
101000.00101 = 1.0100000101 x 25

## Slide 14: DECIMAL FLOATING POINT TO IEEE STANDARD CONVERSION
Step 3. Convert the exponent to a biased exponent
127 + 5 = 132
And convert biased exponent to 8-bit unsigned binary:
13210 = 100001002

## Slide 15: DECIMAL FLOATING POINT TO IEEE STANDARD CONVERSION
Step 4. Store the results from steps 1-3:
Sign Exponent Mantissa
(from step 3) (from step 2)
0 10000100 01000001010000000000000

## Slide 16: FLOATING POINT EXAMPLES
Notes: 16
.6328125-> binary( 101000100000)
Bias= 2k-1-1
K=8
Bias=27-1=127
Base=20
Add Bias= 147=10010011
For 1.6328125x2-20
Bias= -20+127=107=(01101011)2

## Slide 17: FP RANGES
For a 32 bit number
  8 bit exponent (-127 to 128)
  24 bit fraction ( -(1-2-24) to (1-2-24))
Notes: 17

## Slide 18: EXPRESSIBLE NUMBERS
Notes: 18

## Slide 19: IEEE 754 FORMATS
Notes: 19

## Slide 20: IEEE 754
Standard for floating point storage
32 and 64 bit standards
8 and 11 bit exponent respectively
Extended formats (both mantissa and exponent) for intermediate results
Notes: 20

## Slide 22: FP ARITHMETIC +/-
Check for zeros
Align significands (adjusting exponents)
Add or subtract significands
Normalize result
Notes: 22

## Slide 23: FP ARITHMETIC X/
Check for zero
Add/subtract exponents
Multiply/divide significands (watch sign)
Normalize
Round
All intermediate results should be in double length storage
Notes: 23

## Slide 24: FLOATING POINT MULTIPLICATION
Notes: 24

## Slide 25: FLOATING POINT DIVISION
Notes: 25

## Slide 26: REQUIRED READING
Stallings 8th Edition Chapter 9
Stallings 9th Edition Chapter 10
IEEE (Institute of Electrical and Electronics
Engineers) Computer 754 on IEEE Web site
Notes: 26